Transmission snap ring inspection

Good Part Picture

Snap ring is inserted properly. Rotating laser scans in 380 degree circle. Measurement data is converted to grey scale bit map where it is evaluated with PC vision system to determine pass or fail.

Good Part

Accepted output illuminates to green “Pass” Snap ring is the dark grey object in the middle of the screen. It is wavy because the part is held in place by a simple stop, doesn’t require expensive lift and locate. As long as dark grey does not touch the red line part is good.

Good Part Aligned

For visual to operator the image is straightened. This eliminates the wavy look but has no effect on the inspection

Bad Part Picture

Paper clip inserted behind snap ring at 11:00 to create a known bad part

Bad Part

Failure output illuminates to red. Result of scan of bad part. Snap ring is far too left of proper position where paper clip is inserted. The ring gap is visible as slightly lighter shade of gray.

Bad Part Aligned

For visual to operator the image is straightened. This eliminates the wavy look but has no effect on the inspection